## Slide 1: Workshop on MD simulations
2-4.8.2022
EHP-CZ-ICP-3-012
Brno University of Technology

## Slide 2: Trondheim

## Slide 3: Sharing experience and knowledge in multiscale modelling of materials
EHP-CZ-ICP-3-012
-
-
-
-
+
eniac.fme.vutbr.cz

## Slide 4: Organization info
WIFI – SSID: ATOMISTIC PASSWORD: lammpsatomic (EDUROM also available)
Pictures for the funding agency and also for the project.
Do not forget to take some snacks.

## Slide 5: Workshop time schedule

## Slide 6: MLFF – MD with
Petr Šesták
4.8.2022
Workshop MD
EHP-CZ-ICP-3-012
DFT precission
almost

## Slide 7: HPC – High Performance Computing
Czech National Supercomputing Centre – IT4I (www.it4i.cz)
MD or DFT large systems are preformed
at HPC facilities.
You always reach to some point where your simulations
overwhelm capability you local PC.

## Slide 8: HPC – High Performance Computing
https://www.it4i.cz/en/research/research-flagships

## Slide 9: HPC – High Performance Computing
#!/bin/bash
#PBS -N NAMEJOB
#PBS -l nodes=1:ppn=64:epyc7551
#PBS -l mem=120gb
#PBS -q default
##PBS -l walltime=2:00:00
cd $PBS_O_WORKDIR
module add vasp-6.3.0-openmpi-4.1.0
mpirun vasp_std >log.txt

## Slide 10: HPC – High Performance Computing

## Slide 11: HPC – High Performance Computing
https://www.it4i.cz/en/infrastructure/karolina

## Slide 12: Plan
Comparison MD and DFT – advantages and disadvantages.
Simple introduction into AIMD – Ab initio molecular dynamics.
How to speed up AIMD via on the fly machine learned force fields.
How to generate machine learned force fields database.
Classic MD with MLFF interactions.

## Slide 13: Multiscale modeling
length
discipline
quantum mechanics
atomistic model
microstructure
continuum model
ab initio
molecular dynamics
finite elements
nm
m
mm
m
physics – chemistry – mat. science – engineering

## Slide 14: Reactions from audience of experimentalists
I believe in DFT calculations but I do not believe in DFT models.
MD potentials can reflects behavior they were tested for.
Precision must be improved!
We need quantum computers!

## Slide 15: Comparison MD with DFT
The authors have to read paper describing the Tersoff potential again because is not able to reproduce interaction in their simulations.

## Slide 16: Comparison MD with DFT
-
-
-
-
Kotoul M. et al., 2019: Ab Initio Aided Strain Gradient Elasticity Theory in Prediction of Nanocomponent Fracture. MECHANICS OF MATERIALS 136, p. 103074-1 - 10

## Slide 17
How to get DFT precision into MD??

## Slide 18: If you don’t do it, you are a dead ship in the water!
Webinar available at:
https://www.materialsdesign.com/ webinars/recorded/ugm-2021-kresse

## Slide 19: Why LAMMPS and MLFF?

## Slide 20
Kotoul M. et al., 2019: Ab Initio Aided Strain Gradient Elasticity Theory in Prediction of Nanocomponent Fracture. MECHANICS OF MATERIALS 136, p. 103074-1 - 10
Comparison MD and DFT

## Slide 21: Ab initio simulations and molecular dynamics
molecular dynamics | ab initio
easy – based on Newton mechanics | results from Quantum Mechanics
simulations of large scale system with planar defects, temperature | magnetic, optical, electrical, etc. characteristics
fast | accuracy, no input data needed
potentials require calibration | no temperature – simul. at absolute zero temp.
potentials for all interaction – Ni-Ni, Ni-Ti, etc. | limited to small systems (approx. 100-1000 atoms)
 | standard DFT no vdW but has been impl.
requires HPC (High Performance Computing) | requires HPC (High Performance Computing)
Ab initio is very often used for calibration of MD potentials.
-
-
-
-

## Slide 22: DFT self-consistent cycle
Initial Guess of  (r)
Calculate efective potential
Solve Kohn-Sham Equations
Evaluate the ellectron density & total energy
Converged ?
NOT YET?
LETS DO
ANOTHER
STEP!
OUTPUT QUANTITIES
,…..

## Slide 23: Ab initio methods (first principles)
computational codes
  VASP (Vienna Ab initio Simulation Package) – pseudopotentials (www.vasp.at)
    commercial license
    the most used ab initio code in the world
    available pseudopotentials are very well tested
    hybrid pseudopotentials
  Abinit – pseudopotentials (www.abinit.org)
    free under GNU license
    generation of pseudopotentials by users
    some extra features than other codes (Linear Response Functions - direct calculation of phonon spectra, elastic constants, etc.)
    very good parallelization (using multithread program run)
  Wien2k – all electron (no pseudopot.) (www.wien2k.at)
    commercial license
    computationally more demanding than VASP or Abinit
    good parallelization
    no pseudopotential – all electron code
pseudopotentials
  PAW (Projector Augmented Waves), ultra-soft, norm-conserving
  exchange – correlation energy:
    LDA – Local Density Approximation
    GGA BPE – Berdew Burke Ernzerhof
    GGA PW – Perdew Wang
MLFF capability!!!

## Slide 24: VASP – Vienna Ab initio Simulation Package
www.vasp.at

## Slide 25
AIMD
-
-
-
-
+

## Slide 26
ATOMS MOVES ALSO IN AB INITIO

## Slide 27: MD fundamental scheme
structure – initial position and velocities
topology – molecular description
force fields – potential functions V of interactions
compute forces
solve Newton equation of motion
output – position, velocities energies
update r and v in repeating in N steps
forces are determined from the DFT calculations

## Slide 28: AIMD – ab initio molecular dynamics
AIMD
Taking disadvantages from both approaches (ab initio and MD), small cell, CPU time consuming, limited number of MD steps (small time period).
Advances: temperature included, no potential needed, magnetism, high precision.
VASP – Vienna Ab initio Simulation Package (license needed).
Simulation cell at least 100 atoms. My recommendation is 200 – 400 atoms.
-
-
-
-
+

## Slide 29: Characteristics of AIMD
small simulation space
large requirements of CPU power
limited capabilities when compared to the classic MD
up to approx. 500 atoms.
HPC required

## Slide 30: Affected by the simulation cell size
Simulation cell size strongly affect temperature fluctuation.
116 atoms
2900 atoms
23200 atoms

## Slide 31: How I can decrease temperature oscillations?
Look to SMASS parameter and play with it.
https://www.researchgate.net/post/How-can-I-reduce-temperature-oscillation-in-NVT-ensemble-simulation-of-FPMD

## Slide 32: Types of ab initio MD
Classical motion
atom velocity according to classical mechanics
Damped MD
mostly used as a geometry optimizer
Quantum motion
unknown to us

## Slide 33: Training set – the most important choice
AIMD
MLFF

## Slide 34
MLFF
-
-
-
-
+

## Slide 35
As part of the VASP code released in February, 2022.

## Slide 36: On the fly machine learned force fields

## Slide 37: On the fly machine learned force fields
They are not new. They are developing for almost 20 years.
In many cases the ML potentials requires user interactions – some calibration.
Now ML was implemented as a tool for learning without any user interaction.

## Slide 38: Perspective: Machine learning potentials for atomistic simulations
Behler, Jörg. “Perspective: Machine Learning Potentials for Atomistic Simulations.” The Journal of Chemical Physics, vol. 145, no. 17, 7 Nov. 2016, p. 170901, 10.1063/1.4966192.
‌
ML potentials have been available only for low-dimensional systems.
Several different ML approaches suitable for high-dimensional systems containing thousands
of atoms have now become available.
recommended reading

## Slide 39: On the fly machine learning
✦ 10-1000x faster than the classic AIMD
✦ be careful about characteristic related to electronic structure as they are not included (magnetism, etc.)
✦ number of skipped steps cannot be predicted -> difficult guess of CPU time

## Slide 40: What we achieved since releasing in February?

## Slide 41: Tin GB segregation

## Slide 42: Tin GB segregation

## Slide 43: Tin GB segregation
Trained MLFFs are independent to GB type.

## Slide 44: Tin GB segregation

## Slide 45: On the fly machine learned force fields
MLFF – machine learned force fields
Five order magnitude faster than ab initio.
With MLFF almost ab initio accuracy.
Stored quantities: forces between atoms, total energy and stress tensor.
Be careful regarding magnetism and characteristics strongly related to electronic structure.
Advantages: temperature, large simulation cells, extraordinary speed.
-
-
-
-
+

## Slide 46: On the fly machine learned force fields

## Slide 47: How to plan your AIMD
create training system
minimize it
heat up the structure (NpT or NVT)
equilibrate
continue with simulations

## Slide 48: Training set – the most important choice
Do not use super cell containing bulk.
We achieved a very good MLFFs trained on a super cells with grain boundary.
At least 100 atoms.
Type of GBs doesn’t play any role.
Simulation cell at least 5 Angstroms length.

## Slide 49
Let’s go to make same examples
-
-
-
-
+

## Slide 50: Training set – the most important choice – W Σ5 GB (310)

## Slide 51: Starting the learning procedure for MLFF
Copy the data from /workshop to you home directory.
Download the structure file POSCAR.
Use VESTA or OVITO to visualize the straining structure for AIMD with on the fly machine learning.
Look into INCAR file. The are notes for the input variables.
Do not any change of POTCAR and leave it as it is. The file contains PAW pseudopotential of tungsten.
Start your simulation with on the fly learning forces and generate ML_ABN and ML_FFN files.
Enter command “qsub run.sh”.

## Slide 52: Examine obtained results
Look how many steps were performed by the DFT calculation and how many from the MLFF dataset.
  [grep rms OSZICAR |wc –l]
Print temperature vs. number of steps.
Print pressure vs number of steps.
Use VESTA or OVITO to visualize the straining structure for AIMD with on the fly machine learning.

## Slide 53: Can MLFF reflect hydrostatic strain?
Go to directory and start the MLFF as well as the DFT simulation for comparison.
Get data via the present script.
Print them and compare, e.g. SciDAVis.

## Slide 54: Bulk moduli?
Go to directory and start the MLFF as well as the DFT simulation for comparison.
Get data via the present script.
Print them and compare with the DFT results (also available under DFT directory) and experiments.
https://en.wikipedia.org/wiki/Bulk_modulus

## Slide 55: Thank you!
www.eeagrants.org Facebook, Twitter, LinkedIn, Instagram YouTube: EEANorwayGrants Mail: info-fmo@efta.int